## Slide 1
Chapter 6 Wireless and Mobile Networks
Computer Networking: A Top Down Approach 6th edition Jim Kurose, Keith Ross Addison-Wesley March 2012
A note on the use of these ppt slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2012
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 2: Ch. 6: Wireless and Mobile Networks
Background:
# wireless (mobile) phone subscribers now exceeds # wired phone subscribers (5-to-1)!
# wireless Internet-connected devices equals # wireline Internet-connected devices
  laptops, Internet-enabled phones promise anytime untethered Internet access
two important (but different) challenges
  wireless: communication over wireless link
  mobility: handling the mobile user who changes point of attachment to network

## Slide 3: Chapter 6 outline
6.1 Introduction
Wireless
6.2 Wireless links, characteristics
  CDMA
6.3 IEEE 802.11 wireless LANs (“Wi-Fi”)
6.4 Cellular Internet Access
  architecture
  standards (e.g., GSM)
Mobility
6.5 Principles: addressing and routing to mobile users
6.6 Mobile IP
6.7 Handling mobility in cellular networks
6.8 Mobility and higher-layer protocols
6.9 Summary

## Slide 4: Elements of a wireless network
network
infrastructure

## Slide 5: Elements of a wireless network
wireless hosts
laptop, smartphone
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility
network
infrastructure

## Slide 6: Elements of a wireless network
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points
network
infrastructure

## Slide 7: Elements of a wireless network
wireless link
typically used to connect mobile(s) to base station
also used as backbone link
multiple access protocol coordinates link access
various data rates, transmission distance
network
infrastructure

## Slide 8: Characteristics of selected wireless links
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
2G: IS-95, CDMA, GSM
2.5G: UMTS/WCDMA, CDMA2000
802.15
802.11b
802.11a,g
3G: UMTS/WCDMA-HSPDA, CDMA2000-1xEVDO
4G: LTE WIMAX
802.11a,g point-to-point
200
802.11n
Data rate (Mbps)
GSM(Global System for Mobile Communications)

## Slide 9: Elements of a wireless network
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network
network
infrastructure

## Slide 10: Elements of a wireless network
ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: route among themselves

## Slide 11: Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to
base station (WiFi,
WiMAX, cellular)
which connects to
larger Internet
no base station, no
connection to larger
Internet (Bluetooth,
ad hoc nets)
host may have to
relay through several
wireless nodes to
connect to larger
Internet: mesh net
no base station, no
connection to larger
Internet. May have to
relay to reach other
a given wireless node
MANET, VANET.
Mobile Ad hoc Networks (MANET) and Vehicular Ad hoc Networks (VANET) are some of the most promising fields of research and development of wireless network.

## Slide 12: Chapter 6 outline
6.1 Introduction
Wireless
6.2 Wireless links, characteristics
  CDMA
6.3 IEEE 802.11 wireless LANs (“Wi-Fi”)
6.4 Cellular Internet Access
  architecture
  standards (e.g., GSM)
Mobility
6.5 Principles: addressing and routing to mobile users
6.6 Mobile IP
6.7 Handling mobility in cellular networks
6.8 Mobility and higher-layer protocols
6.9 Summary

## Slide 13: Wireless Link Characteristics (1)
important differences from wired link ….
  decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
  interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
  multipath propagation: radio signal reflects off objects ground, arriving ad destination at slightly different times
…. make communication across (even a point to point) wireless link much more “difficult”

## Slide 14: Wireless network characteristics
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal attenuation:
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B

## Slide 15: Chapter 6 outline
6.1 Introduction
Wireless
6.2 Wireless links, characteristics
  CDMA
6.3 IEEE 802.11 wireless LANs (“Wi-Fi”)
6.4 Cellular Internet Access
  architecture
  standards (e.g., GSM)
Mobility
6.5 Principles: addressing and routing to mobile users
6.6 Mobile IP
6.7 Handling mobility in cellular networks
6.8 Mobility and higher-layer protocols
6.9 Summary

## Slide 16: IEEE 802.11 Wireless LAN
802.11b
2.4-5 GHz unlicensed spectrum
up to 11 Mbps
direct sequence spread spectrum (DSSS) in physical layer
802.11a
  5-6 GHz range
  up to 54 Mbps
802.11g
  2.4-5 GHz range
  up to 54 Mbps
802.11n: multiple antennae
  2.4-5 GHz range
  up to 200 Mbps
all use CSMA/CA for multiple access
all have base-station and ad-hoc network versions

## Slide 17: 802.11 LAN architecture
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
hub, switch
or router

## Slide 18: 802.11: Channels, association
802.11b: 2.4GHz-2.485GHz spectrum divided into 11 channels at different frequencies
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
host: must associate with an AP
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with
  may perform authentication [Chapter 8]
  will typically run DHCP to get IP address in AP’s subnet

## Slide 19: 802.11: passive/active scanning
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
3
1
passive scanning:
beacon frames sent from APs
association Request frame sent: H1 to selected AP
association Response frame sent from selected AP to H1
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
2
3
4
active scanning:
Probe Request frame broadcast from H1
Probe Response frames sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent from selected AP to H1

## Slide 20: IEEE 802.11: multiple access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with ongoing transmission by other node
802.11: no collision detection!
  difficult to receive (sense collisions) when transmitting due to weak received signals (fading)
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/C(ollision)A(voidance)
space
A
B
C
A
B
C
A’s signal
strength
C’s signal
strength

## Slide 21: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2
802.11 receiver
- if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
sender
receiver
DIFS
data
SIFS
ACK
DIFS (Distributed Inter-Frame Space)
SIFS (Short Interframe Space )

## Slide 22: Avoiding collisions (more)
idea: allow sender to “reserve” channel rather than random access of data frames: avoid collisions of long data frames
sender first transmits small request-to-send (RTS) packets to Base Station using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
CTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions
avoid data frame collisions completely
using small reservation packets!

## Slide 23: Collision Avoidance: RTS-CTS exchange
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer

## Slide 24: 802.11 frame: addressing
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 1: MAC address
of wireless host or AP
to receive this frame
Address 3: MAC address
of router interface to which AP is attached
Address 4: used only in ad hoc mode

## Slide 25
Internet
router
H1
R1
AP MAC addr H1 MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
R1 MAC addr H1 MAC addr
dest. address
source address
802.3 frame
802.11 frame: addressing
802.3 is a standard specification for Ethernet, a method of physical communication in a local area network (LAN),

## Slide 26
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Type
From
AP
Subtype
To
AP
More
frag
WEP
More
data
Power
mgt
Retry
Rsvd
Protocol
version
2
2
4
1
1
1
1
1
1
1
1
duration of reserved
transmission time (RTS/CTS)
frame seq #
(for RDT)
frame type
(RTS, CTS, ACK, data)
802.11 frame: more

## Slide 27
802.11: mobility within same subnet
H1 remains in same IP subnet: IP address can remain same
switch: which AP is associated with H1?
  self-learning (Ch. 5): switch will see frame from H1 and “remember” which switch port can be used to reach H1
H1
BBS 2
BBS 1

## Slide 28
power management
node-to-AP: “I am going to sleep until next beacon frame”
  AP knows not to transmit frames to this node
  node wakes up before next beacon frame
beacon frame: contains list of mobiles with AP-to-mobile frames waiting to be sent
  node will stay awake if AP-to-mobile frames to be sent; otherwise sleep again until next beacon frame
802.11: advanced capabilities

## Slide 29: Wireless Adapter
Used to give wireless network capability to a laptop computer

## Slide 30: Wireless Bridges
Bridges connect networks and are often less expensive than access points. For example, a wireless LAN bridge can interface an Ethernet network directly to a particular access point.
(Access points connect multiple users on a wireless LAN to each other and to a wired network. For example, 20 users equipped with 802.11 network interface cards (NICs) may associate with a single access point that connects to an Ethernet network.) Source: http://www.wi-fiplanet.com/tutorials/article.php/1563991

## Slide 31: Wireless Bridge
Source: Google images

## Slide 32: Wireless Security
1. Change Default Administrator Passwords (and Usernames)
2. Turn on (Compatible) WPA / WEP Encryption
3. Change the Default SSID
4. Enable MAC Address Filtering
5. Disable SSID Broadcast

## Slide 33: Wireless Security
6. Do Not Auto-Connect to Open Wi-Fi Networks
7. Assign Static IP Addresses to Devices
8. Enable Firewalls On Each Computer and the Router
9. Position the Router or Access Point Safely
10. Turn Off the Network During Extended Periods of Non-Use
Source: http://compnetworking.about.com/od/wirelesssecurity/tp/wifisecurity.htm

## Slide 34
M
radius of
coverage
S
S
S
P
P
P
P
M
S
Master device
Slave device
Parked device (inactive)
P
802.15: personal area network
less than 10 m diameter
replacement for cables (mouse, keyboard, headphones)
ad hoc: no infrastructure
master/slaves:
  slaves request permission to send (to master)
  master grants requests
802.15: evolved from Bluetooth specification
  2.4-2.5 GHz radio band
  up to 721 kbps

## Slide 35: Chapter 6 outline
6.1 Introduction
Wireless
6.2 Wireless links, characteristics
  CDMA
6.3 IEEE 802.11 wireless LANs (“Wi-Fi”)
6.4 Cellular Internet access
  architecture
  standards (e.g., GSM)
Mobility
6.5 Principles: addressing and routing to mobile users
6.6 Mobile IP
6.7 Handling mobility in cellular networks
6.8 Mobility and higher-layer protocols
6.9 Summary

## Slide 36
Mobile
Switching
Center
Public telephone
network
Mobile
Switching
Center
Components of cellular network architecture
connects cells to wired tel. net.
manages call setup (more later!)
handles mobility (more later!)
MSC
covers geographical region
base station (BS) analogous to 802.11 AP
mobile users attach to network through BS
air-interface: physical and link layer protocol between mobile and BS
cell
wired network

## Slide 37: Cellular networks: the first hop
Two techniques for sharing mobile-to-BS radio spectrum
combined FDMA/TDMA: divide spectrum in frequency channels, divide each channel into time slots
CDMA: code division multiple access
frequency
bands
time slots

## Slide 38
BSC
BTS
Base transceiver station (BTS)
Base station controller (BSC)
Mobile Switching Center (MSC)
Mobile subscribers
Base station system (BSS)
Legend
2G (voice) network architecture
MSC
Public
telephone
network
Gateway
MSC
G

## Slide 39
3G (voice+data) network architecture
radio
network
controller
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Serving GPRS Support Node (SGSN)
Gateway GPRS Support Node (GGSN)
Public
Internet
GGSN
G
Key insight: new cellular data
network operates in parallel
(except at edge) with existing
cellular voice network
voice network unchanged in core
data network operates in parallel

## Slide 40
radio
network
controller
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Public
Internet
GGSN
G
radio access network
Universal Terrestrial Radio
Access Network (UTRAN)
core network
General Packet Radio Service
(GPRS) Core Network
public
Internet
radio interface
(WCDMA, HSPA)
3G (voice+data) network architecture

## Slide 41: Chapter 6 outline
6.1 Introduction
Wireless
6.2 Wireless links, characteristics
  CDMA
6.3 IEEE 802.11 wireless LANs (“Wi-Fi”)
6.4 Cellular Internet Access
  architecture
  standards (e.g., GSM)
Mobility
6.5 Principles: addressing and routing to mobile users
6.6 Mobile IP
6.7 Handling mobility in cellular networks
6.8 Mobility and higher-layer protocols
6.9 Summary

## Slide 42: What is mobility?
spectrum of mobility, from the network perspective:
no mobility
high mobility
mobile wireless user,
using same access
point
mobile user, passing through multiple access point while maintaining ongoing connections (like cell phone)
mobile user, connecting/ disconnecting from network using DHCP.

## Slide 43: Mobility: vocabulary
wide area network
home network: permanent “home” of mobile
(e.g., 128.119.40/24)
permanent address: address in home network, can always be used to reach mobile
e.g., 128.119.40.186
home agent: entity that will perform mobility functions on behalf of mobile, when mobile is remote

## Slide 44: Mobility: more vocabulary
wide area network
care-of-address: address in visited network.
(e.g., 79,129.13.2)
visited network: network in which mobile currently resides (e.g., 79.129.13/24)
permanent address: remains constant (e.g., 128.119.40.186)
foreign agent: entity in visited network that performs mobility functions on behalf of mobile.
correspondent: wants to communicate with mobile

## Slide 45: How do you contact a mobile friend:
search all phone books?
call her parents?
expect her to let you know where he/she is?
I wonder where Alice moved to?
Consider friend frequently changing addresses, how do you find her?

## Slide 46: Mobility: approaches
let routing handle it: routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange.
  routing tables indicate where each mobile located
  no changes to end-systems
let end-systems handle it:
  indirect routing: communication from correspondent to mobile goes through home agent, then forwarded to remote
  direct routing: correspondent gets foreign address of mobile, sends directly to mobile

## Slide 47: Mobility: approaches
let routing handle it: routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange.
  routing tables indicate where each mobile located
  no changes to end-systems
let end-systems handle it:
  indirect routing: communication from correspondent to mobile goes through home agent, then forwarded to remote
  direct routing: correspondent gets foreign address of mobile, sends directly to mobile
not
scalable
to millions of
mobiles

## Slide 48: Mobility: registration
wide area network
end result:
foreign agent knows about mobile
home agent knows location of mobile
home network
visited network
1
mobile contacts foreign agent on entering visited network
2
foreign agent contacts home agent home: “this mobile is resident in my network”

## Slide 49: Mobility via indirect routing
wide area network
home
network
visited
network
3
2
4
1
correspondent addresses packets using home address of mobile
home agent intercepts packets, forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent

## Slide 50: Indirect Routing: comments
mobile uses two addresses:
  permanent address: used by correspondent (hence mobile location is transparent to correspondent)
  care-of-address: used by home agent to forward datagrams to mobile
foreign agent functions may be done by mobile itself
triangle routing: correspondent-home-network-mobile
  inefficient when
  correspondent, mobile
  are in same network

## Slide 51: Indirect routing: moving between networks
suppose mobile user moves to another network
  registers with new foreign agent
  new foreign agent registers with home agent
  home agent update care-of-address for mobile
  packets continue to be forwarded to mobile (but with new care-of-address)
mobility, changing foreign networks transparent: on going connections can be maintained!

## Slide 52: Mobility via direct routing
1
2
3
4
home
network
visited
network
correspondent requests, receives foreign address of mobile
correspondent forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent

## Slide 53: Mobility via direct routing: comments
overcome triangle routing problem
non-transparent to correspondent: correspondent must get care-of-address from home agent
  what if mobile changes visited network?
1
2
3
4

## Slide 54: Accommodating mobility with direct routing
wide area network
1
foreign net visited
at session start
anchor
foreign
agent
2
4
new foreign
agent
3
correspondent
agent
correspondent
new
foreign
network
anchor foreign agent: FA in first visited network
data always routed first to anchor FA
when mobile moves: new FA arranges to have data forwarded from old FA (chaining)
5

## Slide 55: Chapter 6 outline
6.1 Introduction
Wireless
6.2 Wireless links, characteristics
  CDMA
6.3 IEEE 802.11 wireless LANs (“Wi-Fi”)
6.4 Cellular Internet Access
  architecture
  standards (e.g., GSM)
Mobility
6.5 Principles: addressing and routing to mobile users
6.6 Mobile IP
6.7 Handling mobility in cellular networks
6.8 Mobility and higher-layer protocols
6.9 Summary

## Slide 56: Mobile IP
RFC 3344
has many features we’ve seen:
  home agents, foreign agents, foreign-agent registration, care-of-addresses, encapsulation (packet-within-a-packet)
three components to standard:
  indirect routing of datagrams
  agent discovery
  registration with home agent

## Slide 57: Mobile IP: indirect routing
Permanent address: 128.119.40.186
Care-of address: 79.129.13.2
dest: 128.119.40.186
packet sent by correspondent
dest: 79.129.13.2
dest: 128.119.40.186
packet sent by home agent to foreign agent: a packet within a packet
dest: 128.119.40.186
foreign-agent-to-mobile packet

## Slide 58: Mobile IP: agent discovery
agent advertisement: foreign/home agents advertise service by broadcasting ICMP messages (typefield = 9)
R bit: registration required
H,F bits: home and/or foreign agent

## Slide 59: Mobile IP: registration example
visited network: 79.129.13/24
home agent
HA: 128.119.40.7
foreign agent
COA: 79.129.13.2
mobile agent
MA: 128.119.40.186
registration req.
COA: 79.129.13.2
HA: 128.119.40.7
MA: 128.119.40.186
Lifetime: 9999
identification:714
….
registration reply
HA: 128.119.40.7
MA: 128.119.40.186
Lifetime: 4999
Identification: 714
encapsulation format
….
registration reply
HA: 128.119.40.7
MA: 128.119.40.186
Lifetime: 4999
Identification: 714
….
time
ICMP agent adv.
COA: 79.129.13.2
….
registration req.
COA: 79.129.13.2
HA: 128.119.40.7
MA: 128.119.40.186
Lifetime: 9999
identification: 714
encapsulation format
….

## Slide 60
Components of cellular network architecture
correspondent
MSC
MSC
MSC
MSC
MSC
wired public telephone
network
different cellular networks,
operated by different providers
recall:

## Slide 61: Handling mobility in cellular networks
home network: network of cellular provider you subscribe to (e.g., Sprint PCS, Verizon)
  home location register (HLR): database in home network containing permanent cell phone #, profile information (services, preferences, billing), information about current location (could be in another network)
visited network: network in which mobile currently resides
  visitor location register (VLR): database with entry for each user currently in network
  could be home network

## Slide 62
Public switched
telephone
network
mobile
user
home
Mobile
Switching
Center
HLR
home
network
visited
network
correspondent
Mobile
Switching
Center
VLR
GSM: indirect routing to mobile
1
call routed
to home network
2
home MSC consults HLR,
gets roaming number of
mobile in visited network
3
home MSC sets up 2nd leg of call
to MSC in visited network
4
MSC in visited network completes
call through base station to mobile

## Slide 63
Mobile
Switching
Center
VLR
old BSS
new BSS
old
routing
new
routing
GSM: handoff with common MSC
handoff goal: route call via new base station (without interruption)
reasons for handoff:
  stronger signal to/from new BSS (continuing connectivity, less battery drain)
  load balance: free up channel in current BSS
  GSM doesnt mandate why to perform handoff (policy), only how (mechanism)
handoff initiated by old BSS

## Slide 64
Mobile
Switching
Center
VLR
old BSS
1
3
2
4
5
6
7
8
new BSS
1. old BSS informs MSC of impending handoff, provides list of 1+ new BSSs
2. MSC sets up path (allocates resources) to new BSS
3. new BSS allocates radio channel for use by mobile
4. new BSS signals MSC, old BSS: ready
5. old BSS tells mobile: perform handoff to new BSS
6. mobile, new BSS signal to activate new channel
7. mobile signals via new BSS to MSC: handoff complete. MSC reroutes call
8 MSC-old-BSS resources released
GSM: handoff with common MSC

## Slide 65
home network
Home MSC
PSTN
correspondent
MSC
anchor MSC
MSC
MSC
(a) before handoff
GSM: handoff between MSCs
anchor MSC: first MSC visited during call
  call remains routed through anchor MSC
new MSCs add on to end of MSC chain as mobile moves to new MSC
optional path minimization step to shorten multi-MSC chain

## Slide 66
home network
Home MSC
PSTN
correspondent
MSC
anchor MSC
MSC
MSC
(b) after handoff
anchor MSC: first MSC visited during call
  call remains routed through anchor MSC
new MSCs add on to end of MSC chain as mobile moves to new MSC
optional path minimization step to shorten multi-MSC chain
GSM: handoff between MSCs

## Slide 67: Mobility: GSM versus Mobile IP
GSM element |  | Comment on GSM element | Mobile IP element | 
Home system | Network to which mobile user’s permanent phone number belongs |  |  | Home network
Gateway Mobile Switching Center, or “home MSC”. Home Location Register (HLR) | Home MSC: point of contact to obtain routable address of mobile user. HLR: database in home system containing permanent phone number, profile information, current location of mobile user, subscription information |  |  | Home agent
Visited System | Network other than home system where mobile user is currently residing |  |  | Visited network
Visited Mobile services Switching Center. Visitor Location Record (VLR) | Visited MSC: responsible for setting up calls to/from mobile nodes in cells associated with MSC. VLR: temporary database entry in visited system, containing subscription information for each visiting mobile user |  |  | Foreign agent
Mobile Station Roaming Number (MSRN), or “roaming number” | Routable address for telephone call segment between home MSC and visited MSC, visible to neither the mobile nor the correspondent. |  |  | Care-of-address

## Slide 68: Wireless, mobility: impact on higher layer protocols
logically, impact should be minimal …
  best effort service model remains unchanged
  TCP and UDP can (and do) run over wireless, mobile
… but performance-wise:
  packet loss/delay due to bit-errors (discarded packets, delays for link-layer retransmissions), and handoff
  TCP interprets loss as congestion, will decrease congestion window un-necessarily
  delay impairments for real-time traffic
  limited bandwidth of wireless links

## Slide 69: Chapter 6 summary
Wireless
wireless links:
  capacity, distance
  channel impairments
  CDMA
IEEE 802.11 (“Wi-Fi”)
  CSMA/CA reflects wireless channel characteristics
cellular access
  architecture
  standards (e.g., GSM, 3G, 4G LTE)
Mobility
principles: addressing, routing to mobile users
  home, visited networks
  direct, indirect routing
  care-of-addresses
case studies
  mobile IP
  mobility in GSM
impact on higher-layer protocols